n                          n                                                      n                          n

| nOtes: Most rotary valves are available in various sizes from 150 mm [6 in] through 700 mm [28 in]. Refer to specification sheets for full details. | Plastics | Chemicals | Minerals | Food | Pharma |
| --- | --- | --- | --- | --- | --- |
| NFPA Version is subject to the rotary valve‘s material of construction and the product being handled. 1 ¦ Vented shear protector not required on vacuum or gravity applications. 2 ¦ A vented shear protector or inlet shear plow may be required on valves handling hard pellets or large granules. 3 ¦ A vented shear protector may be required on valves handling non-permeable powders to dissipate leakage air on pressure systems applications. 4 ¦ A leakage gas separator may be required on valves handling non-permeable powders to dissipate leakage air on pressure systems applications. 5 ¦ For products being pre-dosed into the valves by controlled feed (consult factory for proper application of the leakage gas separator). 6 ¦ For small granular products (less than 1 mm) and soft pellets allowing for degradation. |  |  |  |  |  |

|  | Aeropass | WET | Seal Tite Diverter | WGV | WHK | WZK | WEK | Flap Diverter | Wye Gate Diverter | WYK | WRK | DWR | Orifice Slide Gate |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Powders | n |  | n | n | n | n |  | n | n | n | n | n | n 1 |
| Pellets / Granular Products | n | n | n | n | n | n | n | n | n |  | n | n | n 1 |
| Pressure bar (g) [psi (g)] | 0.8 [12] | 6 [87] | N/A - Gravity | 1 [15] | 3 [43] | 5 [72] | 6 [87] | 1.4 [20] | 1 [15] | 5 [72] | 4 [58] | 1 [15] | 5.5 [80] |
| Hygienic Version |  |  |  |  |  |  |  |  |  | n |  |  |  |
| CIP Version |  |  |  |  |  |  |  |  |  | n |  |  |  |
| Quick Cleaning |  |  |  |  |  |  |  |  |  | n |  |  |  |
| For use in ATEX zones |  | n |  |  |  | n |  | n |  | n | n | n | n |

nOtes:

Several models are available with electric actuators, contact factory for  questions.

1 | Special service inlet recommended.

Plastics                 Chemicals                    Minerals                        Food                Pharma

# Text boxes

|  | Dilute Phase & Metering | high Pressure / Dense Phase |
| --- | --- | --- |
|  | ZZB | HD [imperial] ZHD [metric] | BT | MD | MD 1820 | ZXD | ZRD | ZKD | ZVB | ZVD | ZXQ | ZVH |
| Powders | n | n 1 ¦ 3 | n 1 ¦ 3 | n 1 ¦ 3 | n 1 ¦ 3 | n 4 ¦ 5 | n 4 ¦ 5 | n |  | n | n 5 |  |
| Pellets / Granular Products | 6 | 2 |  | 2 | 2 |  |  |  | n | n |  | n |
| Blow-through Rotary Valve |  |  | n |  |  | n |  |  |  |  | n |  |
| Drop-through Rotary Valve | n | n |  | n | n |  | n | n | n | n |  | n |
| Pressure bar (g) [psi (g)] | 0.2 [3] 1.0 [15] optional | 0.8 [12] | 0.8 [12] | 1.4 [20] | 1.4 [20] | 1.5 [21] | 1.5 [21] | 1.5 [21] | 1.5 [21] | 1.5 [21] | 3.5 [50] | 3.5 [50] |
| Hygienic Version | n |  |  |  |  | n | n |  |  |  |  |  |
| CIP Version |  |  |  |  |  | n | n |  |  |  |  |  |
| Quick Cleaning | n |  |  |  |  | n | n | n | n | n |  | n |
| For use in ATEX zones | n |  |  |  |  | n | n | n | n | n | n | n |
| ATEX protection system |  |  |  |  |  | n | n | n |  | n |  |  |

F-700401-en 2018-02